## Slide 1
Computer Organization تنظيم الحاسوب
Dr. Mahmoud Masadeh
Chapter 5
Large and Fast: Exploiting Memory
Hierarchy

## Slide 2: Large and Fast: Exploiting Memory Hierarchy

## Slide 3: 5.1 Introduction: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 4: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 5: Memory Hierarchy Levels
Block (line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
Hit time: The time required to access a level of the memory hierarchy, including the time needed to determine whether the access is a hit or a miss.
Miss penalty: The time required to fetch a block into a level of the memory hierarchy from the lower level
Memory hierarchy: A structure that uses
multiple levels of memories; as the distance from the processor increases, the size of the memories and the access time both increase.

## Slide 6: 5.2 Memory Technology
Main memory/ Dynamic RAM (DRAM)
Cache Memory/ Static RAM (SRAM)
Flash memory: Nonvolatile memory is the secondary memory in Personal Mobile Devices
Magnetic disk: used to implement the largest and slowest level in the hierarchy in servers
Ideal memory: Access time of SRAM , Capacity and cost/GB of disk

## Slide 7: SRAM Technology
SRAMs are simply integrated circuits that are memory arrays with a single access port that can provide either a read or a write.
SRAMs have a fixed access time to any datum
SRAMs don’t need to refresh and so the access time is very close to the cycle time.
SRAMs typically use six to eight transistors per bit to prevent the information from being disturbed when read.
SRAM needs only minimal power to retain the charge in standby mode.
As long as power is applied, the value can be kept indefinitely

## Slide 8: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back
    Performed on a DRAM “row”

## Slide 9: DRAM Generations

## Slide 10: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
Quad data rate (QDR) DRAM
  Separate DDR inputs and outputs
The latest version of this technology is called DDR4. A DDR4-3200 DRAM can do 3200 million transfers per second, which means it has a 1600-MHz clock.

## Slide 11: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth

## Slide 12: Flash Storage
A type of electrically erasable programmable read-only memory (EEPROM)
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)

## Slide 13: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks

## Slide 14: Disk Storage
Nonvolatile, rotating magnetic storage
Disk surface is divided into concentric circles, called tracks
Sector: One of the segments that make up a track on a magnetic disk; a sector is the smallest amount of information that is read or written on a disk (512 to 4096 bytes).
Cylinder: all the tracks under the heads at a given point on all surfaces.

## Slide 15: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads over the proper track on a disk (3ms to 13ms).
  Rotational latency: the time for the desired sector to rotate under the read/write head (5400 RPM to 15000RPM).
  Data transfer: the time to transfer a block of bits.
  Controller overhead

## Slide 16: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 17: Disk Performance Issues
Manufacturers quote average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Smart disk controller allocate physical sectors on disk
  Present logical sector interface to host
  SCSI, ATA, SATA
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay

## Slide 18: 5.3 The Basics of Cache Memory
Cache: used to refer to any storage managed to take advantage of locality of access
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
Initially, the word Xn is not-exist (miss)
How do we know if the data is present?
Where do we look?
Location of each word in the memory is determined by its address

## Slide 19: Direct Mapped Cache
Direct mapped: each memory location is mapped directly to exactly one location in the cache:
The block in the cache is determined by:
  (Block address) modulo (#Blocks in cache)
8-block $
#Blocks is a power of 2
Use low-order address bits
The $ has 8 words
For the given cache, a given block could be from 4 blocks of the memory

## Slide 20: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
    lower-order bits are used as index into the cache to specify the block address
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0
Handling reads is simpler than handling writes, since reads do not have to change the contents of the cache

## Slide 21: Cache Example

## Slide 22: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 23: Cache Example
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 24: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 25: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 26: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 27: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 28: Address Subdivision
The address is divided into
A tag field, which is used to compare with the value of the tag field of the cache
A cache index, which is used to select the block
Words are aligned to multiples of four bytes. Therefore, the least significant two bits of every address specify a byte within a word.
The total number of bits needed for a cache is a function of the cache size and the address size, because the cache includes both the storage for the data and the tags.
The size of the block above was one word (=4 bytes), but normally it is several.
The size of the given cache is 1024 word = 1K word = 4 K Bytes = 4KiB

## Slide 29: Address Subdivision Example
Consider the following situation:
64-bit addresses
A direct-mapped cache
The cache size is 2n blocks, so n bits are used for the index
The block size is 2m words (2m+2 bytes = 2m+5 bits), so m bits are used for the word within the block, and two bits are used for the byte part of the address
The size of the tag field is 64 − (n + m + 2).
The total number of bits in a direct-mapped cache is 2n ×(block size + tag size + valid field size).
Although this is the actual size in bits, the naming convention is to exclude the size of the tag and valid field and to count only the size of the data.
Thus, the cache in previous Figure is called a 4 KiB cache.

## Slide 30: Example 1
word=4 bytes
Block= 4 words= 16 byte =16*8= 128 bit

## Slide 31: Example 2

## Slide 32: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
63
4 bits
6 bits
22 bits

## Slide 33: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution ( Loading a large cache block which contain unnecessary information will cause other useful data to be evicted from the cache into lower levels of the memory hierarchy, degrading performance).
Miss penalty: the time required to fetch the block from the next lower level of the hierarchy and load it into the cache.
The time to fetch the block has two parts:
  The latency to the first word
  The transfer time for the rest of the block.
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 34: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 35: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write-through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 36: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first
Write-back schemes can improve performance, especially when processors can generate writes as fast or faster than the writes can be handled by main memory.
Write-back scheme is more complex to implement than write-through.

## Slide 37: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Write Allocate on miss: fetch the block (The block is fetched from memory and then the appropriate portion of the block is overwritten).
  No Write Allocate on miss/ Write around: don’t fetch the block (update the portion of the block in memory but not put it in the cache)
For write-back
  Usually fetch the block

## Slide 38: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  (256 block x 16 words/block x 4 bytes/word = 16K bytes)
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%
Miss rate is an important characteristic of cache designs.
The ultimate measure is the effect of the memory system on program execution time.

## Slide 39: Example: Intrinsity FastMATH
word=4 bytes
Block= 4 words= 16 byte =16*8= 128 bit
16 x 4 x 8 = 512

## Slide 40: Split / combined cache
Split cache: A scheme in which a level of the memory hierarchy is composed of two independent caches that operate in parallel with each other, with one handling instructions and one handling data.
A combined cache with a total size equal to the sum of the two split caches will usually have a better hit rate.
The miss rate of the split cache is only slightly worse.
Supporting both an instruction and data access simultaneously
  Doubling the cache bandwidth 
  Slightly increased miss rate 
This observation cautions us that we cannot use miss rate as the sole measure of cache performance

## Slide 41: Main Memory Supporting Caches
Use DRAMs for main memory
  Fixed width (e.g., 1 word)
  Connected by fixed-width clocked bus
    Bus clock is typically slower than CPU clock
Example cache block read
  1 bus cycle for address transfer
  15 bus cycles per DRAM access
  1 bus cycle per data transfer
For 4-word block, 1-word-wide DRAM
  Miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  Bandwidth = 16 bytes / 65 cycles = 0.25 B/cycle

## Slide 42: 5.4 Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:

## Slide 43: 5.4 Measuring Cache Performance

## Slide 44: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Determine: how much faster a processor would run with a perfect cache that never missed
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2 (Instruction miss cycles = I×2%×100 = 2.00×I)
  D-cache: 0.36 × 0.04 × 100 = 1.44 (Data miss cycles = I×36%×4%×100 = 1.44×I)
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 45: Cache Performance Example
What happens if the processor is made faster, but the memory system is not?
Suppose we speed-up the computer in the previous example by reducing its CPI from 2 to 1 without changing the clock rate, which might be done with an improved pipeline.
The system with cache misses would then have a CPI of 1 + 3.44 = 4.44
The system with the perfect cache would be 4.44/1 = 4.44 times as fast.
  The amount of execution time spent on memory stalls was 3.44/ 5.44 = 63%
  Now, the amount of execution time spent on memory stalls is 3.44/ 4.44 = 77%

## Slide 46: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock,
  Hit time = 1 cycle,
  Miss penalty = 20 cycles,
  I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 47: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 48: Associative Caches
Direct mapping: A block can go in exactly one place in the cache
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once to find the required block
  Parallel search by having comparator per entry (expensive)
The middle range of designs between direct mapped and fully associative is called set associative.

## Slide 49: Associative Caches
Set-associative cache: A cache that has a fixed number of locations (at least two) where each block can be placed.
n-way set associative
Each set contains n entries  there is n locations for a block
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)
  compare with all the tags of all the elements of the set

## Slide 50: Associative Cache Example

## Slide 51: Spectrum of Associativity
For a cache with 8 entries/blocks
Increasing the degree of associativity will decrease the miss rate 
Increasing the degree of associativity will increase the hit time 

## Slide 52: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
Direct mapped
For each block address, determine the cache block
The direct-mapped cache generates five misses for the five accesses

## Slide 53: Associativity Example
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
2-way set associative
First, determine to which set each block address maps
Set-associative caches usually replace the least recently used block within a set; that is, the block that was used furthest in the past is replaced.
The two-way set-associative cache has four misses, one less than the direct-mapped cache

## Slide 54: Associativity Example
Fully associative
has four cache blocks (in a single set);
Any memory block can be stored in any cache block.
Has the best performance, with only three misses:
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 55: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 56: Set Associative Cache Organization
The index value is used to select the set containing the address of interest.
The tags of all the blocks in the set must be searched.

## Slide 57: Fully-Associative Cache Organization
In a fully associative cache, there is effectively only one set, and all the blocks must be checked in parallel.
Thus, there is no index, and the entire address, excluding the block offset, is compared against the tag of every block
In a direct-mapped cache, only a single comparator is needed, because the entry can be in only one block, and we access the cache simply by indexing.

## Slide 58: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity
Fully Associative: all blocks are candidates for replacement

## Slide 59: Size of Tags versus Set Associativity
Block size= 4 Word=16Bytes
Cache size = 4K block
Direct Mapping:
#Sets = # Blocks
#Sets = 4K
2-Way Set Associative
#Sets = 2K
4-Way Set Associative
#Sets = 1K
Fully Associative
#Sets = 1

## Slide 60: Multilevel Caches
Used to reduce miss penalty
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
If the second-level cache contains the desired data, the miss penalty for the first-level cache will be essentially the access time of the second-level cache
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 61: Performance of Multilevel Caches
Given
  CPU base CPI = 1, clock rate = 4GHz  clock period=0.25ns
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 62: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 63: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time  shorter clock cycle
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 64: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 65: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access

## Slide 66: 5.5 Dependable Memory Hierarchy
Fault: failure of a component
  May or may not lead to system failure
Failures can be permanent or intermittent
This leads to two related terms:
  reliability and availability.
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 67: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
A related term is annual failure rate (AFR), which is just the percentage of devices that would be expected to fail in a year for a given MTTF
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance using redundancy, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 68: Hardware failures
Hardware failures are typically characterized by a bath tub curve.
The chance of a hardware failure is high during the initial life of the module.
The failure rate during the rated
useful life of the product is fairly low.
Once the end of the life is reached,
failure rate of modules increases again.
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 69: Causes of Hardware failures
Design failures: Take place due to inherent design flaws in the system. In a well-designed system this class of failures should make a very small contribution to the total number of failures.
Infant Mortality: This class of failures cause newly manufactured hardware to fail. Can be attributed to manufacturing problems like poor soldering, leaking capacitor etc. These failures should not be present in systems leaving the factory as these faults will show up in factory system burn in tests.
Random Failures: Can occur during the entire life of a hardware module. Can lead to system failures. Redundancy is provided to recover from this class of failures.
Wear Out: Once a hardware module has reached the end of its useful life, degradation of component characteristics will cause hardware modules to fail. This type of faults can be weeded out by preventive maintenance and routing of hardware.
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 70: System Availability
System Availability is calculated by modeling the system as an interconnection of parts in series and parallel.
The following rules are used to decide if components should be placed in series or parallel:
If failure of a part leads to the combination becoming inoperable, the two parts are considered to be operating in series
If failure of a part leads to the other part taking over the operations of the failed part, the two parts are considered to be operating in parallel.
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 71: Availability in Series
Two parts X and Y are considered to be operating in series if failure of either of the parts results in failure of the combination.
The combined system is operational only if both Part X and Part Y are available.
From this it follows that the combined availability is a product of the availability of the two parts.
The combined availability is shown by A = Ax Ay
Thus,the combined availability of two components in series is always lower than the availability of its individual components.
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 72: Availability in Parallel
Two parts are considered to be operating in parallel if the combination is considered failed when both parts fail.
The combined availability is 1 - (both parts are unavailable).
The combined availability is shown by A = 1 - (1-Ax )2
Thus, the combined availability of two components in parallel is always much higher than the availability of its individual components.
Notes: https://www.eventhelix.com/fault-handling/reliability-availability-basics/

## Slide 73: MTTF vs. AFR of Disks

## Slide 74: 5.7 Virtual Memory
Virtual memory A technique that uses main memory as a “cache” for secondary storage (disk) .
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault
Physical address An address in main memory.
Virtual address An address that corresponds to a location in virtual space and is translated by address mapping to a physical address when memory is accessed.

## Slide 75: Address Translation
Fixed-size pages (e.g., 4K)
It is possible for a virtual page to be absent from main memory and not be mapped to a physical address; in that case, the page resides on disk.
Physical pages can be shared by having two virtual addresses point to the same physical address.
DRAM
Flash
Magnetic Disk
The physical memory is 1 TiB, or 240 bytes, which needs a 40-bit address

## Slide 76: Address Translation
Virtual memory provides relocation.
Relocation maps the virtual addresses used by a program to different physical addresses before the addresses are used to access memory.
This relocation allows us to load the program anywhere in main memory.
Virtual memory systems eliminating the need to find a contiguous block of memory to allocate to a program; instead, the operating system needs only to find enough pages in main memory.

## Slide 77: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Pages should be large enough to try to amortize the high access time
  Fully associative placement
  Smart replacement algorithms
  Write-through will not work for virtual memory, since writes take too long.
    Instead, virtual memory systems use write-back.

## Slide 78: Page Tables
Store placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 79: Translation Using a Page Table
The hardware can form a physical address using
  The page table register,
  The virtual address,
  The indicated page table
The virtual address space is 248 bytes, or 256 TiB.
The physical address space is 240 bytes, which allows main memory of up to 1 TiB.
If RISC-V used a single page table as shown in this figure, the number of entries in the page table would be 236, or about 64 billion entries.
Page size = 4KBit
We’ll see what RISC-V does to reduce the number of entries shortly.

## Slide 80: Page Fault
If the valid bit for a virtual page is off, a page fault occurs.
The operating system must be given control.
This transfer is done with the exception mechanism, which we saw in Chapter 4.
Swap space: The space on the disk reserved for the full virtual memory space of a process.

## Slide 81: Page Table
With hundreds of processes running, each with its own page table, a large space is required for address translation
Therefore, various techniques can reduce the size of address table, including:
  Keep a limit register that restricts the size of the page table for a given process.
  The use of two separate page tables and two separate limits, which breaks the address space into two segments.
  Applying a hashing function to the virtual address so that the size of the page table equals the size of the number of physical pages in main memory.
  Allow the page tables to be paged
  Using multiple levels of page tables (this is the solution that RISC-V uses to reduce the memory footprint of address translation)

## Slide 82: Page Table
RISC-V uses four levels of tables to translate a 48-bit virtual address into a 40-bit physical address
RISC-V uses four levels of tables to translate a 48-bit virtual address into a 40-bit physical address
Notes: https://www.youtube.com/watch?v=Z4kSOv49GNc
https://www.youtube.com/watch?v=qcBIvnQt0Bw&list=PLiwt1iVUib9s2Uo5BeYmwkDFUh70fJPxX

## Slide 83: Mapping Pages to Storage

## Slide 84: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 85: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access (get the data)
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 86: Fast Translation Using a TLB

## Slide 87: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 88: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not present
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur

## Slide 89: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction

## Slide 90: The Intrinsity FastMATH TLB
The memory system uses 4 KiB pages and a 32-bit address space
The virtual page number is 20 bits long.
The physical address is the same size as the virtual address.
The TLB contains 16 entries, it is fully associative, and it is shared between the instruction and data references.
Each entry is 64 bits wide and contains a 20-bit tag (which is the virtual page number for that TLB entry), the corresponding physical page number (also 20 bits), a valid bit, a dirty bit, and other bookkeeping bits.

## Slide 91: TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address