## Slide 1
Computer Organization تنظيم الحاسوب
Dr. Mahmoud Masadeh
Chapter 4

## Slide 2: The Processor

## Slide 3: 4.1 Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two RISC-V implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: load doubleword (ld) and store doubleword (sd)
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq
This subset does not include all the integer instructions, e.g., shift, multiply, and divide, nor does it include any floating-point instructions.
  It illustrates the key principles used in creating a datapath and designing the control.

## Slide 4: Instruction Execution
For instructions of various types, the first two operations are similar:
  Send the program counter (PC) to the instruction memory and fetch the instruction.
  Read one or two registers, using fields of the instruction to select the registers to read.
    For the ld instruction, we need to read only one register, but most other instructions require reading two registers.
Then, depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
A memory-reference instruction will need to access the memory either to read data for a load or write data for a store.
An arithmetic-logical or load instruction must write the data from the ALU or memory back into a register.
A conditional branch instruction, we may need to change the next instruction address based on the comparison; otherwise, the PC should be incremented by four to get the address of the subsequent instruction

## Slide 5: An abstract view of the RISC-V CPU

## Slide 6: Multiplexers
Can’t just join wires together
  Use multiplexers/ Data Selector

## Slide 7: Control

## Slide 8: Control
The control lines are set based primarily on information taken from the instruction being executed.
Several of the units must be controlled depending on the type of instruction.
  the data memory must read on a load and write on a store.
  The register file must be written only on a load or an arithmetic-logical instruction.
A control unit, which has the instruction as an input, is used to determine how to set the control lines for the functional units and two of the multiplexors.
The top multiplixer determines whether PC + 4 or the branch destination address is written into the PC, is set based on the Zero output of the ALU, which is used to perform the comparison of a beq instruction.

## Slide 9: 4.2 Logic Design Conventions
The datapath elements in the RISC-V implementation consist of two different types of logic elements:
  elements that operate on data values: combinational
  elements that contain state
The instruction and data memories, as well as the registers, are all examples of state elements.

## Slide 10: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 11: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
Clocking methodology: The approach used to determine when data are valid and stable relative to the clock.
D
Clk
Q
Clk
D
Q

## Slide 12: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
Edge-triggered clocking: A clocking scheme in which all state changes occur on a clock edge.
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 13: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period
  asserted The signal is logically high or true.
  deasserted The signal is logically low or false.

## Slide 14: 4.3 Building a Datapath
64-bit register
Increment by 4 for next instruction
datapath element: A unit used to operate on or hold data within a processor. In the RISC-V implementation, the datapath elements include the instruction and data memories, the register file, the ALU, and adders.
program counter (PC) :The register containing the address of the instruction in the program being executed.

## Slide 15: R-Format Instructions /arithmetic-logical instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
Register file A state
element that consists
of a set of registers.
Register file

## Slide 16: Load/Store Instructions
Have the general form of : ld x1, offset(x2) or sd x1, offset(x2)
Read register operands
Compute a memory address by adding the base register, which is x2, to the 12-bit signed offset field contained in the instruction.
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 17: Branch Instructions
The beq instruction has three operands:
  two registers that are compared for equality
  a 12-bit offset used to compute the branch target address relative to the branch instruction address
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value
The base for the branch address calculation is the address of the branch instruction.
Thus, the branch datapath must do two operations:
  compute the branch target address
  test the register contents

## Slide 18: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 19: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 20: R-Type/Load/Store Datapath

## Slide 21: Full Datapath

## Slide 22: Elaboration

## Slide 23: 4.4 Simple Implementation Scheme
In this section, we look at what might be thought of as a simple implementation of our RISC-V subset.
We build this simple implementation using the datapath of the last section and adding a simple control function.
This simple implementation covers:
  load doubleword (ld),
  store doubleword (sd),
  branch if equal (beq),
  the arithmetic-logical instructions add, sub, and, and or.

## Slide 24: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on opcode
We can generate the 4-bit ALU control input using a small control unit that has as inputs the funct7 and funct3 fields of the instruction and a 2-bit control field, which we call ALUOp.
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract

## Slide 25: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | Opcode field | ALU function | ALU control
ld | 00 | load register | XXXXXXXXXXX | add | 0010
sd | 00 | store register | XXXXXXXXXXX | add | 0010
beq | 01 | branch on equal | XXXXXXXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001

## Slide 26: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
The main control unit generates the ALUOp bits, which then are used as input to the ALU control that generates the actual signals to control the ALU unit. This style of multi-levels of decoding is a common implementation technique.
Using multiple levels of control can reduce the size of the main control unit.
Using several smaller control units may also potentially reduce the latency of the control unit.

## Slide 27: The Main Control Unit
Control signals derived from instruction
The 4 ALU control bits (called Operation)
The four instruction classes
(arithmetic, load, store, and conditional branch)
use four different instruction formats.

## Slide 28: The Main Control Unit
There are several major observations about
this instruction format that we will rely on:
The opcode field, is always in bits 6:0.
Depending on the opcode, the funct3 field (bits 14:12) and funct7 field (bits 31:25) serve as an extended opcode field.
The first register operand is always in bit positions 19:15 (rs1) for R-type instructions and branch instructions. This field also specifies the base register for load and store instructions.
The second register operand is always in bit positions 24:20 (rs2) for R-type instructions and branch instructions. This field also specifies the register operand that gets copied to memory for store instructions.
Another operand can also be a 12-bit offset for branch or load-store instructions.
The destination register is always in bit positions 11:7 (rd) for R-type instructions and load instructions.

## Slide 29: Translating RISC-V Assembly Language into Machine Language.. ch2
a

## Slide 30: Datapath with Control

## Slide 31: Datapath with multiplexors and control lines
This Figure shows:
Six single-bit control lines
2-bit ALUOp control signal

## Slide 32: The effect of each of the six control signals

## Slide 33: Control lines are instruction dependent

## Slide 34: The simple datapath with the control unit

## Slide 35: R-Type Instruction

## Slide 36: Load Instruction

## Slide 37: Branch-on-Equal Instruction

## Slide 38: Finalizing Control
The penalty for using the single-cycle design with a fixed clock cycle is significant, but might be considered acceptable for this small instruction set.
Historically, early computers with very simple instruction sets did use this implementation technique.
With floating-point unit or an instruction set with more complex instructions, this single-cycle design wouldn’t work well at all.

## Slide 39: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 40: 4.5 Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/0.5n + 1.5 ≈ 4 = number of stages
(normal conditions and large number of instructions)

## Slide 41: RISC-V Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 42: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 43: Pipeline Performance
Pipelined (Tc= 200ps)
Single-cycle (Tc= 800ps)

## Slide 44: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 45: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage

## Slide 46: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 47: 1-Structural Hazards
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 48: 2-Data Hazards
An instruction depends on completion of data access by a previous instruction
  add x19, x0, x1 sub x2, x19, x3

## Slide 49: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 50: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 51: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction

## Slide 52: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for a = b + e; c = b + f;
ld x1, 0(x0)
ld x2, 8(x0)
add x3, x1, x2
sd x3, 24(x0)
ld x4, 16(x0)
add x5, x1, x4
sd x5, 32(x0)
stall
stall
ld x1, 0(x0)
ld x2, 8(x0)
ld x4, 16(x0)
add x3, x1, x2
sd x3, 24(x0)
add x5, x1, x4
sd x5, 32(x0)
11 cycles
13 cycles

## Slide 53: 3-Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 54: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 55: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In RISC-V pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 56: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 57: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 58: Pipeline Summary
Stall due to a load-use data hazard of the ld result
Avoid
stalling in the third
instruction for the
read-after-write data
hazard on x11 by
forwarding the add result.
It need not stall, even without forwarding

## Slide 59: 4.6 RISC-V Pipelined Datapath
WB
MEM
Right-to-left flow leads to hazards

## Slide 60: RISC-V Pipelined Datapath
Returning to our laundry analogy, clothes move through the line, and they never move backward.
There are, however, two exceptions to this left-to-right flow of instructions:
  The write-back stage, which places the result back into the register file in the middle of the datapath
  The selection of the next value of the PC, choosing between the incremented PC and the branch address from the MEM stage
Data flowing from right to left do not affect the current instruction; these reverse data movements influence only later instructions in the pipeline.
The first right-to-left flow of data can lead to data hazards and the second leads to control hazards.

## Slide 61: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 62: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store
Highlight the right half of registers or memory when they are being read and highlight the left half when they are being written.

## Slide 63: IF for Load, Store, …
    The instruction being read from memory using the address in the PC and then being placed in the IF/ID pipeline register.
    The PC address is incremented by 4 and then written back into the PC to be ready for the next clock cycle.
    This PC is also saved in the IF/ID pipeline register in case it is needed later for an instruction, such as beq.
    The computer cannot know which type of instruction is being fetched, so it must prepare for any instruction, passing potentially needed information down the pipeline.

## Slide 64: ID for Load, Store, …
    The instruction portion of the IF/ID pipeline register supplying the immediate field, which is sign-extended to 64 bits, and the register numbers to read the two registers.
    All three values are stored in the ID/EX pipeline register, along with the PC address.
    We again transfer everything that might be needed by any instruction during a later clock cycle.

## Slide 65: EX for Load
    The load instruction reads the contents of a register and the sign-extended immediate from the ID/EX pipeline register and adds them using the ALU.
    That sum is placed in the EX/MEM pipeline register.

## Slide 66: MEM for Load
    The load instruction reading the data memory using the address from the EX/MEM pipeline
    register and loading the data into the MEM/WB pipeline register.

## Slide 67: WB for Load
Wrong register number
    The final step: reading the data from the MEM/WB pipeline register and writing it into the register file in the middle of the figure.

## Slide 68: Corrected Datapath for Load

## Slide 69: The Full data path for load instruction

## Slide 70: EX for Store

## Slide 71: MEM for Store

## Slide 72: WB for Store

## Slide 73: Multi-Cycle Pipeline Diagram
Pipelining can be difficult to master, since many instructions are simultaneously executing in a single datapath in every clock cycle.
To aid understanding, there are two basic styles of pipeline figures:
  multiple-clock-cycle pipeline diagrams
  single-clock-cycle pipeline diagrams
The multiple-clock-cycle diagrams are simpler but do not contain all the details.

## Slide 74: Multi-Cycle Pipeline Diagram
Form showing resource usage
ld x10, 40(x1)
sub x11, x2, x3
add x12, x3, x4
ld x13, 48(x1)
add x14, x5, x6

## Slide 75: Multi-Cycle Pipeline Diagram
Traditional form: use the name of each stage

## Slide 82: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 83: Pipelined Control (Simplified)
Label the control lines in the existing datapath.
We assume that the PC is written on each clock cycle, so there is no separate write signal for the PC.
Also, the pipeline registers are also written during each clock cycle.

## Slide 84: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation
We can divide the control lines into five groups according to the pipeline stage.

## Slide 85: Pipelined Control
Instruction fetch: The control signals to read instruction memory and to write the PC are always asserted, so there is nothing special to control in this pipeline stage.
Instruction decode/register file read: The two source registers are always in the same location in the RISC-V instruction formats, so there is nothing special to control in this pipeline stage.

## Slide 86: Pipelined Control
Execution/address calculation: The signals to be set are ALUOp and ALUSrc. The signals select the ALU operation and either Read data 2 or a sign-extended immediate as inputs to the ALU.
Memory access: The control lines set in this stage are Branch, MemRead, and MemWrite.
The branch if equal, load, and store instructions set these signals, respectively.
Recall that PCSrc selects the next sequential address unless control asserts Branch and the ALU result was 0.

## Slide 87: Pipelined Control
Write-back: The two control lines are MemtoReg, which decides between sending the ALU result or the memory value to the register file, and RegWrite, which writes the chosen value.

## Slide 88: Pipelined Control
The ALU control bits are set depending on the ALUOp control bits and the different opcodes for the R-type instruction.
The values of the control lines have been shuffled into three groups corresponding to the last three pipeline stages

## Slide 89: 4.7 Data Hazards: Forwarding versus Stalling
Consider this sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 90: Dependencies & Forwarding
What happens when a register is read and written in the same clock cycle?
We assume that the write is in the first half of the clock cycle and the read is in the second half, so the read delivers what is written.
We consider only the challenge of forwarding to an operation in the EX stage, which may be either an ALU operation or an effective address calculation.
This means that when an instruction tries to use a register in its EX stage that an earlier instruction intends to write in its WB stage, we actually need the values as inputs to the ALU.

## Slide 91: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 92: Detection Dependency

## Slide 93: Detecting the Need to Forward
Some instructions do not write registers.
Thus, only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 94: Forwarding Paths

## Slide 95: Forwarding Paths

## Slide 96: Forwarding Conditions
Mux control | Source | Explanation
ForwardA = 00 | ID/EX | The first ALU operand comes from the register file.
ForwardA = 10 | EX/MEM | The first ALU operand is forwarded from the prior ALU result.
ForwardA = 01 | MEM/WB | The first ALU operand is forwarded from data memory or an earlier ALU result.
ForwardB = 00 | ID/EX | The second ALU operand comes from the register file.
ForwardB = 10 | EX/MEM | The second ALU operand is forwarded from the prior ALU result.
ForwardB = 01 | MEM/WB | The second ALU operand is forwarded from data memory or an earlier ALU result.

## Slide 97: EX hazard
This case forwards the result from the previous instruction to either input of the ALU.
If the previous instruction is going to write to the register file, and the write register number matches the read register number of ALU inputs A or B, provided it is not register 0, then steer the multiplexor to pick the value instead from the pipeline register EX/MEM.

## Slide 98: MEM Hazard
As mentioned above, there is no hazard in the WB stage, because we assume that the register file supplies the correct result if the instruction in the ID stage reads the same register written by the instruction in the WB stage.
Such a register file performs another form of forwarding, but it occurs within the register file.

## Slide 99: 1.10 Fallacies and Pitfalls
Amdahl’s Law: A rule stating that the performance enhancement possible with a given improvement is limited by the amount that the improved feature is used. It is a quantitative version of the law of diminishing returns.

## Slide 100: Double Data Hazard
Consider the sequence (summing a vector of numbers in a single register):
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
There is a potential data hazards between the result of the instruction in the WB stage, the result of the instruction in the MEM stage, and the source operand of the instruction in the ALU stage
Thus, the result should be forwarded from the MEM stage because the result in the MEM stage is the more recent result.
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 101: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRs1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRs2))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 102: Datapath with Forwarding to resolve hazards

## Slide 103: Load-Use Hazard Detection
When an instruction tries to read a register following a load instruction that writes the same register, then forwarding cannot solve the problem
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2
Load-use hazard when
ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs2))
If detected, stall and insert bubble. Then
forward.
We need a hazard detection unit.

## Slide 104: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 105: Load-Use Data Hazard

## Slide 106: Datapath with Hazard Detection
The forwarding unit controls the ALU multiplexors to replace the value from a general-purpose register with the value from the proper pipeline register.
The hazard detection unit controls the writing of the PC and IF/ID registers plus the multiplexor that chooses between the real control values and all 0s.
The hazard detection unit stalls and deasserts the control fields if the load-use hazard test above is true

## Slide 107: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 108: 4.8 Control/Branch Hazards
If branch outcome determined in MEM
Flush these instructions
(Set control values to 0)
PC

## Slide 109: Reducing Branch Delay
Control hazards are relatively simple to understand, they occur less frequently than data hazards, and there is nothing as effective against control hazards as forwarding is against data hazards.
We will look at two schemes for resolving control hazards and one optimization to improve these schemes

## Slide 110: Assume Branch Not Taken
Stalling until the branch is complete is too slow.
One improvement over branch stalling is to predict that the conditional branch will not be taken and thus continue execution down the sequential instruction stream.
To discard instructions, we merely change the original control values to 0s, much as we did to stall for a load-use data hazard.

## Slide 111: Assume Branch Not Taken
Also, we must change the three instructions in the IF, ID, and EX stages when the branch reaches the MEM stage.
Discarding instructions, then, means we must be able to flush instructions in the IF, ID, and EX stages of the pipeline.
To flush instructions in the IF stage, we add a control line, called IF.Flush, that zeros the instruction field of the IF/ID pipeline register.
Clearing the register transforms the fetched instruction into a nop, an instruction that has no action and changes no state.

## Slide 112: Reducing Branch Delay
Move hardware to determine outcome to ID stage rather than EX
  Target address adder
  Register comparator (XORing individual bit positions of two registers and ORing the XORed result)
Example: branch taken
  36: sub x10, x4, x8 40: beq x1, x3, 16 // PC-relative branch // to 40+16*2=72 44: and x12, x2, x5 48: orr x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)

## Slide 113: Example: Branch Taken

## Slide 114: Example: Branch Taken

## Slide 115: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add x4, x5, x6
add x1, x2, x3
beq x1, x4, target
Can resolve using forwarding

## Slide 116: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add x4, $x5, $x6
lw x1, addr
beq x1, x4, target

## Slide 117: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw x1, addr
beq x1, x0, target

## Slide 118: Dynamic Branch Prediction
The time that is wasted in case of a branch misprediction is equal to the number of stages in the pipeline from the fetch stage to the execute stage.
Modern microprocessors tend to have quite long pipelines so that the misprediction delay is between 10 and 20 clock cycles.
As a result, making a pipeline longer increases the need for a more advanced branch predictor
Dynamic branch prediction: look up the address of the instruction to see if the conditional branch was taken the last time this instruction was executed, and, if so, to begin fetching new instructions from the same place as the last time.
Branch prediction buffer or branch history table: a small memory indexed by the lower portion of the address of the branch instruction. The memory contains a bit that says whether the branch was recently taken or not.

## Slide 119: Dynamic Branch Prediction
Prediction is just a hint that we hope is correct, so fetching begins in the predicted direction. If the hint turns out to be wrong, the incorrectly predicted instructions are deleted, the prediction bit is inverted and stored back, and the proper sequence is fetched and executed.
This simple 1-bit prediction scheme has a performance shortcoming: even if a conditional branch is almost always taken, we can predict incorrectly twice, rather than once, when it is not taken.
The following example shows this dilemma.

## Slide 120: Dynamic Branch Prediction

## Slide 121: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 122: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 123: Dynamic Branch Prediction
branch target buffer: A structure that caches the destination PC or destination instruction for a branch. It is usually organized as a cache with tags, making it more costly than a simple prediction buffer.
correlating predictor: A branch predictor that combines local behavior of a particular branch and global information about the behavior of some recent number of executed branches.

## Slide 124: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 125: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 126: Pipeline summary

## Slide 127: 4.9 Exceptions and Interrupts
Control is the most challenging aspect of processor design: it is both the hardest part to get right and fast.
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 128: Exceptions and Interrupts

## Slide 129: Interrupts
When CPU receives any interrupt signal from peripheral(s) which are requesting its services, it stops its current execution and program control is transferred to a sub-routine by generating CALL signal and after executing subroutine by generating RET signal again program control is transferred to main program from where it had stopped.
Hardware and Software Interrupts
  When CPU receive interrupt signals through pins (hardware) of CPU, they are known as Hardware Interrupts
  Software Interrupts are those which are inserted in between the program which means these are mnemonics of CPU

## Slide 130: Interrupts
Vectored and Non-Vectored Interrupts
  Vectored Interrupts are those which have fixed vector address.
  Non-Vectored Interrupts (Scalar Interrupt) are those in which vector address is not predefined. The interrupting device gives the address of sub-routine for these interrupts
Maskable and Non-Maskable Interrupts
  Maskable Interrupts are those which can be disabled or ignored by the CPU
  Non-Maskable Interrupts are those which cannot be disabled or ignored by CPU

## Slide 131: Handling Exceptions
The only types of exceptions that our current implementation can generate are:
  Execution of an undefined instruction.
  Hardware malfunction.
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Then transfer control to the operating system at some specified address.
The operating system can then take the appropriate action, which may involve:
  providing some service to the user program,
  taking some predefined action in response to a malfunction,
  or stopping the execution of the program and reporting an error.
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 0000 0000 1C09 0000hex

## Slide 132: An Alternate Mechanism
Vectored Interrupts
  An interrupt for which the address to which control is transferred is determined by the cause of the exception.
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 133: Handling Exceptions
The operating system knows the reason for the exception by the address at which it is initiated.
When the exception is not vectored, as in RISC-V, a single entry point for all exceptions can be used, and the operating system decodes the status register to find the cause.
We can perform the processing required for exceptions by adding a few extra registers and control signals to our basic implementation and by slightly extending control.
Let’s assume that we are implementing the exception system with the single interrupt entry point being the address 0000 0000 1C09 0000hex.

## Slide 134: Handling Exceptions
We will need to add two additional registers to our current RISC-V implementation:
Supervisor Exception Program Counter / SEPC: A 64-bit register used to hold the address of the affected instruction. (Such a register is needed even when exceptions are vectored.)
Supervisor Exception Cause Register /SCAUSE: A register used to record the cause of the exception. In the RISC-V architecture, this register is 64 bits, although most bits are currently unused. Assume there is a field that encodes the two possible exception sources mentioned above, with 2 representing an undefined instruction and 12 representing hardware malfunction.

## Slide 135: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use SEPC to return to program
Otherwise
  Terminate program
  Report error using SEPC, SCAUSE, …

## Slide 136: Exceptions in a Pipeline
A pipelined implementation treats exceptions as another form of control hazard.
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set SEPC and SCAUSE register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 137: Exceptions in a Pipeline
To flush instructions in the ID stage, we use the multiplexor already in the ID stage that zeros control signals for stalls.
A new control signal, called ID.Flush, is ORed with the stall signal from the hazard detection unit to flush during ID.
To flush the instruction in the EX phase, we use a new signal called EX.Flush to cause new multiplexors to zero the control lines.
To start fetching instructions from location 0000 0000 1C09 0000hex, which we are using as the RISC-V exception address, we simply add an additional input to the PC multiplexor that sends 0000 0000 1C09 0000hex to the PC.

## Slide 138: Pipeline with Exceptions

## Slide 139: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in SEPC register
  Identifies causing instruction

## Slide 140: Exception Example

## Slide 141: Exception Example

## Slide 142: Exception Example

## Slide 143: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!
The SEPC register captures the address of the interrupted instructions.
The SCAUSE register records the highest priority exception in a clock cycle if more than one exception occurs.

## Slide 144: Imprecise Exceptions
Imprecise interrupt Also called imprecise exception. Interrupts or exceptions in pipelined computers that are not associated with the exact instruction that was the cause of the interrupt or exception.
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 145: 4.10 What are ILP, DLP, TLP, RLP?
Consider we have extra space on the processor due to miniaturization, how do we use it?
  more processing elements (parallel components)
Code is implicitly sequential, how do we take advantage of the parallel elements?
  ILP – instruction level parallelism (pipelining)
  DLP – data level parallelism (pipelined arithmetic units, loop unrolling)
  TLP – thread-level processing (using multiple processors/cores)
  RLP – request-level processing (multiple processors/cores plus OS help)

## Slide 146: 4.10 Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice

## Slide 147: Multiple Issue
There are two ways to implement a multiple-issue processor, with the major difference being the division of work between the compiler and the hardware.
Static multiple issue /at compile time
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue /during execution
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 148: Speculation
Speculation: An approach whereby the compiler or processor guesses the outcome of an instruction to remove it as a dependence in executing other instructions
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 149: Compiler/Hardware Speculation
Compiler can reorder instructions
e.g., moving an instruction across a branch or a load across a store
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 150: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 151: Static Multiple Issue
Issue packet: The set of instructions that issues together in one clock cycle; the packet may be determined statically by the compiler or dynamically by the processor.
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)
Very Long Instruction Word (VLIW) A style of instruction set architecture that launches many operations that are defined to be independent in a single-wide instruction, typically with many separate opcode fields.

## Slide 152: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 153: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 154: RISC-V with Static Dual Issue
Extra ports in the register file
a separate adder to calculate the effective address for data transfers.

## Slide 155: Hazards in the Dual-Issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x10, x0, x1 ld x2, 0(x10)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 156: Scheduling Example
Schedule this for dual-issue RISC-V
Loop: ld x31,0(x20) // x31=array element add x31,x31,x21 // add scalar in x21 sd x31,0(x20) // store result addi x20,x20,-8 // decrement pointer blt x22,x20,Loop // branch if x22 < x20
 | ALU/branch | Load/store | cycle
Loop: | nop | ld x31,0(x20) | 1
 | addi x20,x20,-8 | nop | 2
 | add x31,x31,x21 | nop | 3
 | blt x22,x20,Loop | sd x31,8(x20) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 157: Loop Unrolling
loop unrolling: A technique to get more performance from loops that access arrays, in which multiple copies of the loop body are made and instructions from different iterations are scheduled together.
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 158: Loop Unrolling Example
Loop: ld x31,0(x20) add x31,x31,x21 sd x31,0(x20) addi x20,x20,-8 blt x22,x20,Loop

## Slide 159: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi x20,x20,-32 | ld x28, 0(x20) | 1
 | nop | ld x29, 24(x20) | 2
 | add x28,x28,x21 | ld x30, 16(x20) | 3
 | add x29,x29,x21 | ld x31, 8(x20) | 4
 | add x30,x30,x21 | sd x28, 32(x20) | 5
 | add x31,x31,x21 | sd x29, 24(x20) | 6
 | nop | sd x30, 16(x20) | 7
 | blt x22,x20,Loop | sd x31, 8(x20) | 8

## Slide 160: Dynamic Multiple Issue
Superscalar: An advanced pipelining technique that enables the processor to execute more than one instruction per clock cycle by selecting them during execution.
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 161: Dynamic Pipeline Scheduling
Dynamic pipeline scheduling: Hardware support for reordering the order of instruction execution to avoid stalls.
Allow the CPU to execute instructions out of order to avoid stalls
But commit result to registers in order
Example, which avoids data hazard:
ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
Can start sub while add is waiting for ld

## Slide 162: Dynamic Pipeline Scheduling
In dynamic pipeline scheduling the pipeline is divided into three major units:
  an instruction fetch and issue unit: fetches instructions, decodes them, and sends each instruction to a corresponding functional unit for execution
  multiple functional units: Each functionalunit has buffers, called reservation stations, which hold the operands and the operation.
  and a commit unit: contain reorder buffer, which is used to supply operands, in much the same way as forwarding logic does in a statically scheduled pipeline

## Slide 163: Dynamic Pipeline Scheduling
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 164: Dynamic Pipeline Scheduling
out-of-order execution: A situation in pipelined execution when an instruction blocked from executing does not cause the following instructions to wait.
in-order commit: A commit in which the results of pipelined execution are written to the programmer visible state in the same order that instructions are fetched.

## Slide 165: Energy Efficiency and Advanced Pipelining

## Slide 166: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall